## Slide 1: The perf_event subsystem
Tomson Li, Yifan Wang, Lien Zhu

## Slide 2: Revisiting HPCs
Hardware Performance Counters measure micro-architectural events
Special purpose registers used for performance analysis
CSE 522S – Operating Systems Organization. Marion Sudvarg, David Ferry, Chris Gill, Brian Kocoloski
ARM Cortex-A53
CPU Core
PMU
CPU Core
PMU
CPU Core
PMU
CPU Core
PMU
L2 Cache

## Slide 3: ARM PMU
PMU
Performance Monitors Control Register
32-bits
Each bit is an individual control
Enable, reset, 32/64-bit mode, report number of counters, etc.
Performance Monitors Cycle Count Register
Performance Monitor Event Counters
and Performance Monitor Event Types
Event type register controls corresponding counter
Reset by setting counter to 0
Enable 64-bit mode by chaining subsequent counters
PMCR
PMCNTR
0-31
32-63
PMEVCNTR0
PMEVTYPER0
PMEVCNTR1
PMEVTYPER1
PMEVCNTR2
PMEVTYPER2
PMEVCNTR3
PMEVTYPER3
PMEVCNTR4
PMEVTYPER4
PMEVCNTR5
PMEVTYPER5
CSE 522S – Operating Systems Organization. Marion Sudvarg, David Ferry, Chris Gill, Brian Kocoloski

## Slide 4: Linux perf_event subsystem abstracts the PMU
The perf_event_open() syscall
The perf user space tool

## Slide 5: The perf user space tool provides a command line interface for interacting with the kernel
Notes: Draw attention to LLC-load-misses

## Slide 6: The perf user space tool provides a command line interface for interacting with the kernel
Notes: Still, the subsystem is riddled with error

## Slide 7: Multiplexing introduces extrapolation error into the subsystem
Events must be time-shared on to counters then extrapolated
Motivates event scheduling
[1] https://developer.arm.com/documentation/ddi0500/j/Performance-Monitor-Unit/About-the-PMU?lang=en
Notes: A significant source of error is due to multiplexing
Raspberry Pi has 6 general purpose counters [1]
Ran 1-6, 12, and 24 events in perf stat –e <events> on stress-ng
LLC-load-misses was the pre-selected event
So multiplexing is quite impactful and how events are assigned to counters is solved by event scheduling algorithms

## Slide 8: The vanilla Event Scheduler algorithm Background
Primitive unit of scheduling is event group
All events in a group must have certain attributes in common
  Pinned vs Flexible
All or None in an event group for success
Event groups are added into a linked list
E1, E2, E3
E4, E5, E6, E7
E8, E9, E10
E11, 12
G1
G2
G3
G4

## Slide 9: The vanilla Event Scheduler algorithm Example
E1, E2, E3
E4, E5, E6, E7
E8, E9, E10
E11, E12
G1
G2
G3
G4
C1 | C2 | C3 | C4 | C5 | C6
E1 | E2 | E3 | x | x | x
Notes: List is traversed head to tail
G2 fails to schedule
Upon failure, the algorithm activates counters for counting and iteration proceeds
Software events fill the rest of counters, but error in hardware event counts is exacerbated
- Linux hrtimer sends multiplexing interrupt for interval

## Slide 10: The Event Scheduler algorithm Example, second iteration
E1, E2, E3
E4, E5, E6, E7
E8, E9, E10
E11, E12
G1
G2
G3
G4
C1 | C2 | C3 | C4 | C5 | C6
E11 | E12 | E4 | E5 | E6 | E7
Notes: - Tail rotates to head
- This time all counters are utilized

## Slide 11: Observations
The algorithm is significantly Inefficient
  Counters are activated as soon as a group fails, which does not consider schedulability of later event groups
E1, E2, E3
E4, E5, E6, E7
E8, E9, E10
E11, E12
G1
G2
G3
G4
C1 | C2 | C3 | C4 | C5 | C6
E1 | E2 | E3 | E8 | E9 | E10
Notes: Once a hardware event group fails to be scheduled, software events are scheduled onto the remaining counters.
This reduces time on PMU for hardware events which exacerbates error from extrapolation
Modifying the event scheduler is difficult, but may not be necessary to see significant improvements

## Slide 12: Key Insight: Not every event is significant
Reducing need for multiplexing would improve accuracy of event counts
Sensitivity analysis can
  inform users of perf user space tool
  reduce extrapolation error
Notes: We can reduce the need to multiplex in the first place by reducing the events that are traced
Transition to Tomson